## Slide 1
NSU RAPID RESPONSE ROBOTIC TELESCOPE
AT FAN MOUNTAIN OBSERVATORY
Carlos Salgado:Department of Physics:NSU

## Slide 2
Rapid Response
Robotic
Telescope
Main Research Goal:
Photometry and Polarimetry of Gamma-Ray Bursts Optical
Afterglows in collaboration with NASA’s Swift and GLAST
missions.
But also
to study all other transient phenomena
Measurement are made in seconds
of object discovery
Telescope can act in fully scripted mode
(no human intervention)

## Slide 3
Covesville, Virginia: 17 miles South of Charlottesville by Road 29

## Slide 4
Charlottesville
29

## Slide 5
24” RRRT
UVA 40”
UVA 31”

## Slide 6
Guest House
31”
40”
NSU RRRT
FAN MOUNTAIN OBSERVATORY

## Slide 7
Telescope: 24” Optical Guidance System, Ritchey-Chretien

## Slide 8
Optical Guidance Systems : RC24-140F
Specs
 Optical System: Ritchey-Chretien
 Primary Diameter: 24.0"
Specular Precision: 1/25, or better, (wave front RMS)
Mirror Substrate Near-zero expansion ceramic
 Focal Ratio: f/8.0
F: 4876.8 mm
 Image Scale 42.1 arc sec/mm
Tube (Open truss) Diameter 29"
Focuser Tube I.D. : 4.2"
 Available Back Focus: 11.5" (+/= 2”)
Secondary Diameter: 8.5"
Sec. Focus Range (electric standard): 12"
Focus Stabilization, w. Al tube Invar 36
 Mounting OGS-140 Equatorial Fork (steel)
Aux. Instrument Cap.: 75 lbs.
R. A. Drive 18" 570 tooth Byers worm gear & ball bearing worm
DEC Drive 15" 360 tooth Byers worm gear & ball bearing worm
Shafts 6.0" Ø (140mm at R. A. bearing ends; 75mm at DEC ends)
Motors Five-phase nano-step / servo
Axis Intersection 72" from base of pier (at 40°)
Fork Swing Clearance 18"
Weight (system) 1025 lbs.
R. A. Counterweights 2 x 5 lbs.
Pier 32" high

## Slide 9
Optical Guidance Systems : RC24-140F
Specs (Cont)
 Pointing error of approx. 30 arc sec RMS or better for 80 degrees from
zenith and less than 20 arc sec RMS 45 degrees around the zenith.
 Tracking/Guiding (RA and Dec)
Sidereal/Moon/Planets/Sun
within 1 arc sec for 300 sec, 0.3 arc sec over 100 sec
able to be controlled with auto-guiding input
tracking rates up to 2 degrees per second for programmed satellite tracking.
slewing rates up to 6 degrees/second (90 degrees in 15 sec)

## Slide 10
MAIN INSTRUMENTATION
Finder-guider
Dual Filter Wheel
Apogee Alta E42 (Back-illuminated)
A.C.E.

## Slide 11
Alta E42
Imaging Photometry and Polarimetry

## Slide 12: Imaging Polarimetry Using Double Refraction
An optically corrected calcite prism produces double polarized images which can be analysed by aperture photometry to give the polarization of each object in the field.
Field of view : 30 min arc (diagonal)
Field of view /pixel: 0.6 sec arc

## Slide 13
Other instruments (already acquired):
CCD Cameras: SBIG - 10E
SBIG – STV
Meade DSI
SBIG Self-guided Spectrograph
SBIG AO7 Adaptive Optics
SBIG Color (8) Filter Wheel
RGB & UBVRI filters
Several eyepieces, filters, …
Telescopes: 12” Meade SC LX200GPS (altazimut) – comp. control
14” Celestron SC (equatorial) – comp. control
16” Meade DST Newtonian (equatorial)
3x 10” Meade SC
8x 8” Meade SC
Software: Hartmann Mask
Lucy-Richardson CCD Sharp
CCD Ops
AIP4WIN (Berry et al.)
IRAF

## Slide 14
Control System (Bisque Software)
MKS 4000 Telescope Motion Control System, (TMCS)
The Sky6, Orchestrate, TPoint, CCDSoft
SBOS - Software Integration
Software Bisque's Observatory Suite (SBOS) is an integrated suite of software
applications designed for complete control of observatory equipment. The core
software applications include:
TheSky6 Professional Edition
CCDSoft CCD Astronomy Software Version 5
TPoint Telescope Pointing Analysis Software
Orchestrate Scripting Software
And these additional applications build on the core to allow remote control of your
observatory:
Internet Astronomy Software Client and Server Applications (for local-area or
wide-area network observatory control).
Browser Astronomy (patent pending) for web-based remote observatory control.
AutomaDome Dome Control Software
These applications include all the functionality necessary to control the hardware at
an observatory, including telescopes, CCD cameras, Autoguiders, video cameras,
SBIG's Adaptive Optics device, color filter wheels, focusers domes, etc. Most main
stream observatory hardware is supported out of the box. In addition, the suite has
standardized application programming interface (API) for hardware communications
allowing the integration of custom observatory hardware by third parties willing to
write their own implementation of the APIs.

## Slide 15
Clamshell
Observatory

## Slide 18
Roll-off Observatory

## Slide 19
Schedule:
Telescope installation by November 2005
Calibrations (about first three months)
Summer 2005: Enclosure construction
Tailpiece design and construction
Start on-site sky studies (Using UVA and NSU telescopes)
Atmospheric extinction coefficients
Seeing and transparencies
Atmospheric variability
 FORM RESEARCH GROUPS (NEXT)

## Slide 20
Research Topics (Groups)
Gamma-Ray Bursts – Optical Afterglows
Near-Earth Objects
Variable Stars
Supernovae Search
Astrophotography
Other Transients
Atmospheric monitors
Education/Outreach